## Slide 1: Microcontroller

## Slide 2: Agenda
Introduction
Hardware Components
Coding

## Slide 3: Arduino / ESP32
Arduino / ESP32 is the go-to gear hobbyists
With Arduino / ESP32, you can control almost everything around you, be it simple LED or giant robots
Basically Arduino / ESP32 are microcontroller boards
Microcontroller is microprocessor with memory, RAM and some other peripheral connected with it.

## Slide 4: Example: Arduino Uno
What does it have?
Microcontroller ATmega328 with 20 MHz, 32 kB flash memory and 2 kB of RAM
14 Digital In/Out pins (6 can be used as PWM)
6 Analog Inputs
A USB Connection
A Power Jack
Reset Button
On-board LED
SCL/SDA pins (Serial Clock/ Serial Data pins)
ATmega328

## Slide 5: Example: Arduino Uno
What does it have?
Microcontroller ATmega328 with 20 MHz, 32 kB flash memory and 2 kB of RAM
14 Digital In/Out pins (6 can be used as PWM)
6 Analog Inputs
A USB Connection
A Power Jack
Reset Button
On-board LED
SCL/SDA pins (Serial Clock/ Serial Data pins)
     ESP32 boards are more powerful, often with 240 MHz dualcore, more memory, WiFi and Bluetooth
ATmega328

## Slide 6: Different Types of Arduino / ESP32
Arduino LilyPad
Arduino Uno
DIY Arduino
ESP32 WROOM 32
ESP32 WROOM 32E N8

## Slide 7: How to Code with Arduino / ESP32
You need to download Arduino IDE (Integrated Development Environment)
Arduino IDE is available for all Mac, Windows and Linux

## Slide 8: How to Code with Arduino / ESP32
You need to download Arduino IDE (Integrated Development Environment)
Arduino IDE is available for all Mac, Windows and Linux
For more complex projects, other IDEs are available, like a VS Code plugin (platform.io)

## Slide 9: Run the Arduino IDE
Once you have downloaded and installed/extracted the folder, you can directly run Arduino.exe, which will take you to its IDE
The IDE will look like the shown screenshot

## Slide 10: Run the Arduino IDE
Once you have downloaded and installed/extracted the folder, you can directly run Arduino.exe, which will take you to its IDE.
The IDE will look like the shown screenshot.
Coding language is C++

## Slide 11: Run the Arduino IDE
Once you have downloaded and installed/extracted the folder, you can directly run Arduino.exe, which will take you to its IDE.
The IDE will look like the shown screenshot.
Coding language is C++
Setup: Code will run once the Arduino / ESP 32 is started
Loop: After setup was called, the loop will run indefinitely

## Slide 12: Inputs vs. Outputs

## Slide 13: Reading (Input) and Writing (Output) Data
The pins can be used to read or write data
  digitalWrite()
  analogWrite()
  digitalRead()
  analogRead()
5 V
0 V
5 V
0 V

## Slide 14: Upload Code: Board Selection
Before uploading your code to the Arduino / ESP32, double check that correct board is selected under Tools  Board

## Slide 15: Upload Code: Serial Port Selection
Before uploading the serial port has to be selected (defines which USB port the Arduino / ESP32 is connected to)

## Slide 16: Upload Code: Upload
Upload code to the Arduino / ESP32
Once uploaded, whenever powered the microcontroller will start executing the code (setup first, then loop)

## Slide 17: Agenda
Introduction
Hardware Components
Coding

## Slide 18: Push Button
When button not pressed, 5 Volts are read on pin 2
When button is pressed, 0 Volt are read on pin 2

## Slide 19: Push Button

## Slide 20: Rotary Encoder
Measure clockwise or counterclockwise rotations
Pin C can be connected to pin A and pin B via sliding contacts

## Slide 21: Rotary Encoder
Measure clockwise or counterclockwise rotations
Pin C can be connected to pin A and pin B via sliding contacts
Pin C: Ground
Pin A and B are measured
Pin A
Pin B

## Slide 22: LEDs
LED type WS2812b
Each Red, Green, Blue (RGB) has a value from 0 – 255 (8 bit)
Ground
Data
5 Volts
 | LED 1 | LED 2 | LED 3 | …
Red | 100 | 0 | 255 | …
Green | 0 | 0 | 255 | …
Blue | 0 | 0 | 255 | …

## Slide 23: LEDs
LED type WS2812b
Each LED can be addressed individually, even with only one data connection
  when data is transmitted to a an LED, which already has old data, the old data is send to the next LED
Ground
Data
5 Volts

## Slide 24: LEDs
LED type WS2812b
Each LED can be addressed individually, even with only one data connection
Ground
Data
5 Volts
LED 1
LED 2
LED 3
Data

## Slide 25: LEDs
LED type WS2812b
Each LED can be addressed individually, even with only one data connection
Ground
Data
5 Volts
LED 1
LED 2
LED 3
R: 255
G: 255
B: 255

## Slide 26: LEDs
LED type WS2812b
Each LED can be addressed individually, even with only one data connection
Ground
Data
5 Volts
LED 1
LED 2
LED 3
R: 255
G: 255
B: 255

## Slide 27: LEDs
LED type WS2812b
Each LED can be addressed individually, even with only one data connection
Ground
Data
5 Volts
LED 1
LED 2
LED 3
R: 255
G: 255
B: 255
R: 0
G: 0
B: 0

## Slide 28: LEDs
LED type WS2812b
Each LED can be addressed individually, even with only one data connection
Ground
Data
5 Volts
LED 1
LED 2
LED 3
R: 255
G: 255
B: 255
R: 0
G: 0
B: 0

## Slide 29: LEDs
LED type WS2812b
Each LED can be addressed individually, even with only one data connection
Ground
Data
5 Volts
LED 1
LED 2
LED 3
R: 255
G: 255
B: 255
R: 0
G: 0
B: 0
R: 100
G: 0
B: 0

## Slide 30: LEDs
LED type WS2812b
Each LED can be addressed individually, even with only one data connection
Ground
Data
5 Volts
LED 1
LED 2
LED 3
R: 255
G: 255
B: 255
R: 0
G: 0
B: 0
R: 100
G: 0
B: 0

## Slide 31: LEDs
LED type WS2812b
Each LED can be addressed individually, even with only one data connection
Ground
Data
5 Volts
LED 1
LED 2
LED 3
R: 255
G: 255
B: 255
R: 0
G: 0
B: 0
R: 100
G: 0
B: 0
 When no new signal is sent for a certain while, all LEDs change colors

## Slide 32: Agenda
Introduction
Hardware Components
Coding

## Slide 33: LEDs: Code Setup 1/2
Library to control the LEDs  FastLED
Define the number of LEDs on our LED strip

## Slide 34: LEDs: Code Setup 1/2
Library to control the LEDs  FastLED
Define the number of LEDs on our LED strip
Define an array that contains our RGB value
CRGB is a data structure from FastLED
  e.g. pixel_buffer[2].r is the red value of the third LED
  Constant values of many different colors are available, e.g. CRGB::YELLOW

## Slide 35: LEDs: Code Setup 1/2
Library to control the LEDs  FastLED
Define the number of LEDs on our LED strip
Define an array that contains our RGB value
CRGB is a data structure from FastLED
  e.g. pixel_buffer[2].r is the red value of the third LED
  Constant values of many different colors are available, e.g. CRGB::YELLOW

## Slide 36: LEDs: Code Setup 2/2
Tell FastLED what LEDs are used, what pin the LED strip is on and what array to use for LED data

## Slide 37: LEDs: Code Setup 2/2
Tell FastLED what LEDs are used, what pin the LED strip is on and what array to use for LED data
Send the pixel_buffer data to the LED strip

## Slide 38: LEDs: Code Setup 2/2
Tell FastLED what LEDs are used, what pin the LED strip is on and what array to use for LED data
Send the pixel_buffer data to the LED strip
Reset the pixel_buffer by setting all values to black

## Slide 39: Star Animation 1/5
Idea: have random single LEDs light up in rainbow colors for a short period of time
Define the number of stars we want
Create an array with possible colors for the star
Using object oriented programming to create a Star class
functions
properties

## Slide 40: Star Animation 2/5
Function 1: random_init

## Slide 41: Star Animation 3/5
Function 2: update

## Slide 42: Star Animation 4/5
Initialization of arrays of Star objects
Setup: initialize each star once
Loop: Update each star and write star color to pixel_buffer

## Slide 43: Star Animation 5/5
More code is added to make the star animation prettier
  Brightness is fading in and out
  Have breaks between a star ends and a new star beginns
  Choosing any of the rainbow colors (wheel function)

## Slide 44: Drop Animation
A colorful raindrop running down the LED strip
Similar structure to Star
  Functions random_init and update
  Parameters for color, position
  Instead of a lifetime, the drop runs through the strip and ends after running out of the strip